## Slide 1: Synergy
Ease the grid. Shrink your bill.
Shamanth Shastry · MHacks 26

## Slide 2: Agenda
01
Problem Statement
02
Tools
03
Demo
04
Value Proposition

## Slide 3: Problem Statement
01

## Slide 4: Electric grids, everyday residents
The resident
Bill says $125. Not which appliance
No way to see what costs what, hour by hour
Advice is generic and never checked
A plug on every outlet is the only fix today
The grid
Overloaded at weekday evenings (3–7 pm peak)
Frequency and voltage drops
Equipment damage, outages
Peaker plants: the dirtiest hours on the grid

## Slide 5: Stakeholders
1
Households
Want a lower bill
Won't install ten sensors
Need advice they can trust
2
Utilities (DTE)
Time-of-day plans need buy-in
Peak demand is the cost driver
Want customers to shift load
3
Grid operators (MISO)
Evening peak strains capacity
Shifted load avoids peakers
Lower emissions per kWh

## Slide 6: Solution: one sensor, every appliance, advice you can verify
1
One sensor
Clamp on the breaker panel. Power + harmonics, every 2 s
→
2
Split by a CNN
Per-appliance usage and cost, labelled as estimated
→
3
Priced advice
3 suggestions a week, in dollars, under the real DTE tariff
→
4
Verified
A week later: did it save? Ranking learns from it

## Slide 7: Tools
02

## Slide 8: Tools
Front end
React + TypeScript + Vite
Sign-in, typed intro, 3 tabs: Home · Actions · Savings
Back end
Python 3.11 + FastAPI (all pricing, all formatting)
PyTorch seq2point CNN (NILM splitter)
LightGBM 7-day forecaster
SpacetimeDB on Maincloud (append-only, reducers)
Gemini 2.5 Flash narrator (JSON schema)
Open-Meteo weather · DTE tariff

## Slide 9: Flow
Sensor
2 s readings
Ingest
validate, batch
Store
SpacetimeDB
CNN
per-appliance
Forecast
7 days, weather
Price
6 templates, DTE
Narrate
Gemini
Tap
device + undo
Verify
a week later
Success score re-ranks next week's suggestions
No model ever emits a dollar: price = kWh × that hour's rate
Devices change only on a tap, with 24 h undo
Gemini gets structured records; every number checked verbatim

## Slide 10: Demo
03

## Slide 11: Demo
Home
This month's bill, day by day
Where the power goes (CNN estimate)
Tap a day for its rundown
Actions
3 priced suggestions, plain English
Take action on precool
Schedule installed on the thermostat
A week later
Advance the demo clock
Savings tab: verified $
Ranking learns what worked

## Slide 12: Value Proposition
04

## Slide 13: Value proposition
1
sensor for the whole house
not one per outlet
3
priced suggestions a week
under your real tariff
$16.10
verified in the demo
measured, not promised
0.99
laptop F1, held-out
CNN with harmonics
Residents: see what each appliance costs, cut it, and confirm the saving
Grid: load moves out of the 3–7 pm peak, fewer peaker hours
Greener homes, one house at a time

## Slide 14: Technical recap
The CNN (NILM)
seq2point: 299-sample window → centre estimate
35 inputs: power, current, PF, 32 harmonics
Shared 5-layer encoder; watts + on/off head × 8 appliances
Split by recording session, never by sample
Laptop F1 0.99 with harmonics vs 0.64 without
Beats the classic CO baseline on 4 appliances
Guardrails
No ML component emits a dollar or CO₂ figure
Gemini: structured in, JSON out, numbers verified verbatim
Device changes only on a tap; schedules expire with the week
Raw readings append-only; ledger never deleted
Verifier uses the forecast that priced the action
Inference in numpy: no PyTorch beside LightGBM

## Slide 15: Ease the grid. Shrink your bill.
Greener homes, one house at a time.
Synergy · Shamanth Shastry